## Slide 1
Proposal Title:
Diagnosing and quantifying uncertainties of
the reanalyzed clouds, precipitation and
radiation budgets over the Arctic and SGP
using combined surface-satellite observations
PI: Xiquan Dong, Uni. of North Dakota
Co-Is: Baike Xi and Aaron Kennedy
Three Graduate Students:
Emily Qiu, first year’s Ph.D student
Erica Dolinar, second year’s MS student
Ron Stenz, second year’s MS student
Both Erica and Ron will work on this
project for their Ph.D degree next fall

## Slide 2: Objectives
Objective 1: Quantifying the uncertainties of reanalyzed Arctic cloud-radiation properties using satellite-surface data
Objective 2: Investigating the reanalyzed hydrological cycle at SGP

## Slide 3
Anticipated Results
We will use an innovative diagnostic method to
quantify the uncertainties of reanalyzed cloud-radiation-precipitation,
compare the five reanalyzed results with observations, find their similarities and differences, and
investigate how these differences relate to large-scale dynamic patterns and variables using the Self Organizing Maps (SOM) method.

## Slide 4: Reanalyses and Datasets
Reanalyses: (i) CFSv3, (ii) 20CR, (iii) MERRA,
(iv) ERA-I, and (v) JRA-25.
Datasets:
a) Satellite observations:
CERES EBAF: TOA and surface radiation fluxes
CERES-MODIS: Cloud properties: CF, LWP/IWP, re.
CloudSat/CALIPSO (CC): CF, LWP/IWP, re.
TRMM and GPCP precipitation products over SGP
b) Surface observations
Cloud-Precipitation Products at SGP: UND hybrid radar/GOES cloud-precipitation product, Oklahoma Mesonet, and NEXRAD Q2.
DOE ARM NSA and SGP cloud and radiation data
BSRN and other surface observations over Arctic

## Slide 5
ALE
BSRN Sites:
Event | Time
Alert (ALE) | 09/2004-08/2013
Barrow (BAR) | 01/1992-02/2010
Eureka (EUR) | 11/2007- 12/2011
Greenland Summit (GRS) | No data available yet
Tikisi (TIK) | 06/2010- 09/2013
Ny-Ålesund (NYA) | 08/1992- 02/2012
BAR
EUR
GRS
TIK
NYA
ARM Sites:
Event | Time
Barrow (BAR) | 05/1998-04/2011
Atqasuk | 06/2000-01/2010
Oliktok | 09/2013-12/2013
Oliktok
Atqasuk
ARM and BSRN Surface Sites

## Slide 6: Objective 1: Quantifying the uncertainties of reanalyzed Arctic cloud-radiation properties
There are two tasks for this Objective
Task 1: : Compare the reanalyzed cloud fractions and TOA/
surface radiation budgets over arctic region using NASA CERES Ed4 results during the period 2000-2011, and CloudSat/CALIPSO (CC) during 2006-2010.
Task 2: Investigate the reanalyzed Cloud and surface radiation fluxes at ARM and BSRN surface sites.
Task 1 will be performed by Ms. Erica Dolinar. She is currently
evaluating CMIP5 CF and radiation budgets using CERES-MODIS and CC.
(Dolinar et al. 2013, Clim Dyn)
Task 2 will be performed by Ms. Emily Qiu. She is currently working on validating CERES-MODIS cloud retrievals using ARM NSA
observations over Arctic region.

## Slide 7: Task 1: : Examples with Satellites
MERRA annual mean CF is 9% higher than CERES-MODIS observed one (72.8% vs. 63.8%), significantly higher during winter (75.7% vs. 50.7%), and lower during summer (68.5% vs. 77.2%). However, MODIS is not perfect.
MODIS
MERRA

## Slide 8
Cloud Fraction Comparison between MODIS and CC
Mean = 76.3%
Mean = 74.9%
Mean = 80.2%
Mean = 0.25%
Mean = 0.08%
During the summer months, CERES-MODIS derived total CFs agree with CloudSat/CALIPSO (CC) very well, in general, remain within 10% of active CC measurements
(Giannecchini, MS thesis, 2012)
Mean = -2.18%
Summer

## Slide 9
CERES-MODIS results agree well with CC across the Greenland and Barents Seas, but over central Arctic region, CERES-MODIS underestimates CFs about 30-40% due to Polar night.
Mean = 73.3%
Mean = 73.4%
Mean = 70.4%
Mean = -18.6%
Mean = -20.0%
Mean = -18.1%
Cloud Fraction Comparison between MODIS and CC
Winter

## Slide 10: Arctic surface radiation budget
Monthly mean surface
downwelling and upwelling LW and SW flux comparisons between CERES EBAF and MERRA over Arctic region during 2000-2010.
The differences in SWdown and LW fluxes are much less than their SWup comparison because MERRA snow/
ice albedo was fixed at 0.6, while the observed ones can be up to 0.8-0.9. (Dong et al. 2013, Clim Dyn)

## Slide 11: Task 2: : Examples with surface
Monthly mean CF from the ARM NSA ceilometer increases from March to May, remains high from May to October, and then decreases from November until the following March. Four of five reanalyses (MERRA, 20CR, CFSR, and ERA-I) have minimal seasonal variations in their reanalyzed CF. They are similar in magnitude to the observed CF from May to October, but have large positive biases (+15% → +40 %) from November to April.
R2 stands out with large negative biases (-35.8%).
(Zib et al. 2012, J Clim)
ARM NSA site

## Slide 12: Task 2: : Examples with surface
With large negative bias in CF, R2 SW-down is much higher and LW_down is much lower than ARM observations.
Other four reanalyzed SW_down and LW_down fluxes agree well with ARM observations except for LW_down winter 20CR.
(Zib et al. 2012, J Clim.)
Summary:
Compared to satellite and surface data, there are large temporal and spatial variations in reanalyses. It is necessary to quantify their biases and uncertainties.
ARM NSA site

## Slide 13: Objective 2: Investigating the reanalyzed hydrological cycle at SGP
We will compare monthly mean cloud fractions and total precipitations from five selected reanalyses with different observational platforms, such as ARM, Oklahoma mesonet, NEXRAD Q2, GPCP, TRMM, and UND hybrid radar/GOES product over the SGP region during the period 1997-2013.
It is challenge to evaluate the reanalyzed lifetime and diurnal cycles of Deep convective systems, and their associated precipitation rate and areal coverage from each reanalysis.
This objective will be performed by Mr. Ron Stenz. He is currently
improving GOES-R precipitation retrievals using UND hybrid radar/GOES product, OK mesonet and NEXRAD Q2 product.
(Stenz et al. 2013, J. Hydrometeo)

## Slide 14: Precipitation comparisons are straighforward
Kennedy et al. 2011, J. Clim
Dong et al 2011, JGR
Kennedy et al 2011, J. Clim

## Slide 15
Ecd
Ccu
CT
Ece
Ece
Ese
Esd
Csu
Ese
NEXRAD
Low-Level
Mid-Level
GOES
Convective
Thick Anvil
Stratiform
Thick Anvil
Deep Cloud
Thin Anvil
Cold Cloud Shield (GOES)
Precipitation
Total Anvil
Total Anvil
Feng et al. (2011) JGR

## Slide 16: Diurnal Cycle of DCS Cloud Fraction
Frequency
Area
CF
Local Noon
Time period:
May-Aug, 2010-2011,
~ 4000 DCSs , hourly data
Domain: SGP Oklahoma
Color lines: CC, SR, AC
Freq: peak right after sunset for CC/SR/AC
Area: AC dominates area cover. CC peaks at late afternoon, SR/AC peak between evening and midnight
Cloud Fraction CF
= Freq. × Area Coverage
Peak of SR/AC CFs consistent with nocturnal MCS over SGP region
Feng et al. 2011
CF
Notes: Introduce each color, will be consistent for this section

## Slide 17: Example of one tracked system using GOES IR temp (last 15 hrs)
Red: cold core (TIR < 215 K)
Blue: cold cloud (TIR < 235 K)
Formation
Mature
Dissipation
The formation-dissipation processes of a DCS
Feng et al. 2012
Notes: Two cold cores developed and split at 8-hr after detection
Mature stage show large areas of depressed TIR and expanding cold cloud area

## Slide 18: Linked tracking results with Hybrid Classification
Red: cold core (TIR < 215 K)
Blue: cold cloud (TIR < 235 K)
Precipitation
Anvil Clouds
Derive statistics for each system using information from hybrid classification
Notes: Matching/Expanding process only change system size, number of systems and life cycles remain intact

## Slide 19: Define Life Cycle Stages
System Equivalent Radius
System Min TIR
1 2 3 4 5
Developing Mature Dissipating
Reason: composite systems with different lifetimes
Based on tendency of system size and TIR
Developing (1, 2)
  Before reaching min TIR
  Warm developing (TIR > 220K)
  Cold developing (TIR < 220K)
Mature (3)
  Min TIR < time < Max Radius
Dissipating (4, 5)
  Cold dissipating
  Warm dissipating
Group all systems based on defined stages

## Slide 20: Work Plan and responsible personnel
2013-2014: Attend NOAA MAPP CRTF Monthly Telecom, and seek collaboration with other team members.
2014-2015
(1) Collect and process all observational and reanalysis datasets those will be used in this study (whole team).
(2) Compare Arctic cloud-radiation results between reanalyses and satellite and surface data (Dolinar, Qiu, Dong, Xi), and develop Arctic SOM (Kennedy)
(3) Compare cloud-precipitation over the ARM SGP region between reanalyses and satellite-surface products (Ron, Dong)
(4) Present the results to scientific meetings, such as AMS, AGU, EGU, and NOAA MAPP and reanalysis related meetings, and submit two papers to refereed journals (whole team).
2015-2016
(5) Find the similarities and differences in Arctic cloud-radiation between reanalyses and datasets, and link these results with large-scale dynamic patterns and variable through SOM technique (whole team).
(6) Evaluate the reanalyzed life and diurnal cycles of Deep convective systems, and their associated precipitation rate and areal coverage from each reanalysis (Ron, Dong)
(7) Present research results to scientific meetings, and submit three papers to refereed journals (whole team).
(8) Hiring web developer to post our results on our webpage (http://faculty.atmos.und.edu/dong/) (Computer assistant, Xi).

## Slide 21
Thanks for your attention!
Questions?

## Slide 22: Backup Slides

## Slide 23: Composite by Life Cycle
Time period: May-Aug, 2010-2011 (hourly data)
Total number of tracked systems: 3995
CC expands quickly in developing stage, reach maximum between cold developing/mature stage
SR/AC size have similar tendency: gradually grow and reach maxima at cold dissipating stage
CC area: 9%, SR area: 18%, AC area:73%
Conv Core (CC)
Strat Rain (SR)
Anvil Cloud (AC)
Size
Notes: Explains box whisker plot, box: 25/75 percentile, whisker: 90%, square: mean, cross: median

## Slide 24: Precipitation Evolution
Precipitation comes almost exclusively from convective rain in developing and mature stage
Stratiform rain gradually becomes more important as system dissipates
CC/PR rain rate evolution similar to sizes
PRCC is 10× PRSR
CC
SR
Volume Rain Fraction (%)
Rain Rate (mm/hr)

## Slide 25: Self Organizing Map (SOM)
SOM is a competitive neutral network. It classifies atmospheric states (P, WS, RH) and links them with cloud and precipitation occurrences which will help us to determine if reanalyzed biases come from model dynamics.
5x7 SOM for January SLP – Hewitson and Crane (2002)
H
L
After creating the feature map, the user can then classify individual samples